## Slide 1: Networking for non-networking engineers – 1/?

## Slide 2: Why?

## Slide 3: Unlearn.. learn

## Slide 4: Challenge: - Computer 1: ”Hello” - Computer 2: “Hello, World!”

## Slide 5
nic-b
nic-a
Notes: Computers don’t send bits.
Computers don’t absolutely don’t packets.
Computers send signal to each others, Modern signals are *Pulses*. Each `pulses` has bits encoded to it. Each signal can represent a `symbol`.
How many “bits“ a flagger can send at a time?
For more on Naval Semaphores flags:: https://en.wikipedia.org/wiki/Flag_semaphore

## Slide 6
H
L
E
L
O
O
D
L
R
W
Notes: Few assumptions we made here:
1- Computer A will only connect to computer B. Specifically, computer A has a dedicated *nic* and *line* to talk to computer B, and vice versa …. for every sender/receiver combination
2- Computer B will get each signal clearly, on first attempt.
These `pulses` travel on faulty lines, often translated to different `pulses` and often spanning the entire planet.
It is important to note, that there is not a “message transmission”. There is no `begin message`.. `send`.. Just symbols from A-->B
For more on Naval Semaphores flags:: https://en.wikipedia.org/wiki/Flag_semaphore

## Slide 7
nic-b
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
Notes: “All problems in computer science can be solved by another level of indirection” , David Wheeler
Data link takes a buffer and *encapsulate* it (aka encap-ed) with:
1- Frame Header: Length
2- Frame Footer: sequence + CRC.
** frames are of agreed upon max size 1500b, or jumpo frames 9000b.. Or protocol specific, as long as sender/receiver know the max length then things should work as expected**
I still need nic+ line for each machine I am connected to. So..
Enter: MAC ADDRESS. A 6 byte (unique on the network). Usually encoded on the NIC itself. Each frame carries source/destination mac addresses
There is not a lot of excitement for software engineers at this level (unless …)
However folks who literally ”connect the world” live and die by these stuff. Imagine ISPs, satellite connections, frame lay or better imagine folks building cross cloud data centers backbone connections
Did we:
– *Really* the addressing problem? What happens if replaced machine B nic?
– Did we solve the scale problem? I mean in theory we can have a wire from machine A to each machine N we want to connect to. But do we have to?
– We – so far – assumed that computers A->B can only send one message at a time .. What if I have multiple applications running on machine B which multiple clients on machine A wants to talk to?
– Did we solve message assured delivery?
– What if I want to send large data?

## Slide 8
nic-b … N
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
SWITCH
Notes: – Did we solve the scale problem? I mean in theory we can have a wire from machine A to each machine N we want to connect to.
Obviously we are not going to wire every machine in our network to every other machine. The solution is to connect them to a switch
1- Is a L2 link( device), that learns the mac address of every machine it is connected to (to each port)
2- It allows machine A to send *frame* to machine B by copying the packet from one switch port to another.
3- **packets are not copied to any other port**
The hubs that you guys are using does not operate like that, every packet is copied to every port connected. Hence if you want to test perf on your personal lab using a hub is generally a bad idea.
Did we:
– We – so far – assumed that computers A->B can only send one message at a time .. What if I have multiple applications running on machine B which multiple clients on machine A wants to talk to?
– Did we solve message assured delivery?
– What if I want to send large data?

## Slide 9: Demo-0: IP->MAC ADDRESS
Notes: (DEMO 0)
Flush arp tables
Ping while tracing
Key Message: arp is used to learn the mac address of connected hosts

## Slide 10
nic-b …
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
Network
Network
Out: *Packet* <HEADER>BUFFER
Notes: – *Really* the addressing problem? What happens if replaced machine B nic? More importantly what happens if computer-b is not directly connected to computer-a
Network layer takes a buffer and encap It with:
1- Header:
*** Source IP
*** Destination IP
*** Fragmentation Handling (ID, FLAG, OFFSET)
*** TTL
*** PROTCOL (TCP, UDP, ICMP) – Those are IP protocol, but where are the likes of SCTP? (it is a transport protocol and is treated like TCP)
As with any wire-format, you should expect `header size` and `total size`
2- Payload
ARP is when layer two trying to create a `frame`, it knows an IP and needs to translate it to MAC. If the mapping is not in cached. It *broadcast* a `WhoHas` (who has <IP> tell <sender>) packet which basically goes to every one connected to the same network. A `reply` message comes back from the owner saying `<IP> is-at <MAC ADDRESS>. There is another approach, when your box comes online can **gratuit-lly say I am <IP> with <MAC>** (Also used when a machine changes its mac).
There are 18 types of ICMP packets, spanning host to host, network configuration, MTU discovery and more
Did we:
– We – so far – assumed that computers A->B can only send one message at a time .. What if I have multiple applications running on machine B which multiple clients on machine A wants to talk to?
– Did we solve message assured delivery?
– What if I want to send large data?

## Slide 11: Demo 1: Sending IP Packets
Notes: View code of ./sender/main.go
Key Messages:
  Packet construction
  Why did we choose golang?
Running the DEMO (because of inability to pipe live tcpdump over ssh)
  Jumo to VM1
  Run step 1

## Slide 12
Receiver
Sender
Receiver
Sender
Receiver
Receiver
Receiver
Sender
Receiver
Receiver
All nodes
unicast
multicast
broadcast
Notes: Unicast: 1:1
Multicast: special address space where senders can `cast` to and receivers can start listening to.
Broadcast: Each network has1 address, and one special address to broadcast to all hosts to network
Note. Multicast and broadcast can work on mac address level as well.
Question: why multicast and broadcast does not work (or very hard to support) in cloud networking?

## Slide 13
Switched Network
Node
Node
Node
Node
Node
Node
Node
Node
Node
switch
switch
switch
router
router
External network
Notes: 1- Each node maintains a table of routes <network expressed as cidr> via <ip>
2- Routes establishes a hope count to destination, smaller # of hops == faster path
3- That means a typical network will have at least one route <anything not internal> via <ip> (This IP has to be ARPed why?)
Routers SNAT ip packets as they go out, WHY? Because as the sender return – response - packet to sender, if it can not reach them it will be dropped.
Router will not DNAT ip packets as it routes them from <external> to <internal>
Segway: inline LB discussions (BRIEF SINCE WE WILL COVER THIS IN NEXT PART).
Knowing what we know so far, how can two routers maintain H/A?
For readers: Advanced routing scenario:
-- Two routers on the network.. Each route to different addresses
-- H/A routers
-- Policy Based Routing

## Slide 14
Router
Node-1
Node-2
Equal-Cost Multi-Path Routing (load balancing)
Packets going to router can be *balanced* to node-1 or node-2. smarter routers can have probes, measure latency etc..
<cidr-x> via node-1-ip
<cidr-x> via node-2-ip
Notes: No *flows* discussion yet

## Slide 15: Demo 2: IP routing demo
Notes: The env prepared for this talk is in fact a routed network.
The linux bridge where all the VMs are connected is a router
the host machine is configured to accept forwarded packets (packets that has dst IP != hostIP)
How does this work:
view the forwarding setting on the host, follow the readme.md file instruction

## Slide 16
network
Router-1
Router-2
Router-n
network
mtu:1500
mtu:1200
fragment
mtu:1500
mtu:1500
mtu:1500
Notes: mtu problem is by product of routing across uknown network. Where one router on the `path` uses mtu less than the others, this router will start fragmenting the packets (chunk a large one to smaller ones) causing transmit penalty across the entire path
There are solutions.. MTU path discovery. An icmp packet with DO-NOT-FRAGEMENT is sent to target host. Any host that can not transmit as is will respond with back with FRAGMENTATION NEEDED – SIZE = XXX

## Slide 17
We are gonna need a bigger ip address space

## Slide 18: Ipv6 vs ipv4
Address is 128bit (23bit for IPv4)
No NAT, because we have plenty of addresses (however we still do NAT, sometimes)
MTU Path Discovery is used by default. IPv6 forces 1280 octets minimum.
QoS packet flags are cleaner
Better neigh discovery
Personal favorite: [Auto configuration] via `neighborhood discovery` (router advertisement, link unreachability etc) mostly via ICMP packets

## Slide 19: What we have learned so far..
We can send packets: receive can make sure that packets are correct via checksums
We can configure via ICMP packets.
We still can’t
  We still can’t address to an `application`, only a `node`
  Ensure packets are delivered.
  Ensure that packets (or assembled) in the right order

## Slide 20
nic-b …
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
Network
Network
Out: *UDP datagram* <HEADER>BUFFER
UDP Transport
UDP
Transport
Out: *Packet* <HEADER>BUFFER
APP
APP
UDP
Notes: UDP datagram has
1- Source Port (16bit)
2- Destination Port (16bit)
3- Packet check sum (16bit)
4- Packet Length (16 bit)
No header length needed (since source and target port are fixed length). Because of this model a state machine is created. Reciever has to “listen” first on a port, before the sender can send anything.
Cool we have solved addressing app, but we didn’t address anything else (assembled in order, nor ensured deliver)

## Slide 21: Demo 3: UDP Demo
Notes: -- run cleanup FIRST
-- step 0
-- then step 1
Show that packets has no ack by just running step 1 only
Key messages
Udp has no connection state machine
No ack, messages will fail and sender will not know
Because of the above UDP has perf advantages (even with limitation) hence it is preferred for gaming, streaming and soon for HTTP/3

## Slide 22
nic-b …
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
Network
Network
Out: *TCP segment* <HEADER>BUFFER
TCP Transport
TCP
Transport
Out: *Packet* <HEADER>BUFFER
APP
APP
TCP
Notes: TCP segement has:
Source Port
Destination Port
Sequence number (first byte in sequence)
Ack (sender can say I ack <seq> receive assumes anything *before* is acked)
Optional parameters (MSS is one of them)
URG: Urgent pointer is valid (nobody uses this)
ACK: Message has ack
PSH: message is data
RST: Reset the connection
SYN: sequence number is valid
FIN: Terminate the connection
Header Length
*Window scaling management* (more on this later)
Question difference between RST and FIN
Notice: Connection State machine

## Slide 23: Connection State Machine
Graceful and non-graceful termination
Sources: https://ipwithease.com/tcp-fin-vs-rst-packets/
https://ubidots.com/blog/how-to-simulate-a-tcpudp-client-using-netcat/
syscall view
3 Way - Handshake

## Slide 24: Demo 4: TCP DEMO
Notes: View ./server/main.go, discuss the connection state machine
-- run step0 (this starts the server)
-- tcpdump port 10020 on a new shell (vm0)
DEMO:
run (vm1) netcat -zv 192.168.99.10 10020
This ^^^ shows the connection state machine in action.
DEMO
Run (VM1) curl -vvv 192.168.99.10:10020

## Slide 25: Faster TCP?
TCP Fast Open: Send data in 1st syn packet (suspect to syn flooding).
Accumulated ack: acks are send for every few segments, not each.
Slow: Sender starts a retransmission counter for every segment. If a segment ack is not received before counter, segment is retransmitted.
Fast Retransmission: receiver receives A, C segments. Sends dup ack for A, sender resents B. receiver acks B and C (3 duplicate acks for segment).

## Slide 26: TCP Congestion Control - 1
Nic Buffer
App
network
Kernel Buffer
Notes: Those buffers are chock points
If nic h/w buffer is full, packets are dropped before even receving them
If kernel buffer is full (or kernel is too busy with other house keeping tasks) then packets are dropped
If app is not picking up datagrams or packets quick enough underlaying buffers will be dropped

## Slide 27: TCP Congestion Control - 2
Two full-duplex endpoints are sending and receiving concurrently.
Sender sends a “rwindow” (tcp segment) and maintains internal “cwindow” (per session).
  rwind: How many bytes I am willing to receive
  cwind: calculated..
cwind calculation (Old Tahoe)
  Start with: MSS, with every ack add one-mss
  After “slow start”, i.e reached a threshold (congestion avoidance): cwnd = cwnd + MSS /cwnd
  When congested (retransmission || packet loss):
    Threshold= 0.5 * cwind
    Cwind=mss
    Go back to slow start
Not so New world: cubic (https://github.com/torvalds/linux/blob/master/net/ipv4/tcp_cubic.c)
New world: Google’s BBR (https://github.com/google/bbr)
Notes: -- Why didn’t we talk about nagle algorithm?
Nagle will lower the total # of segments on the network, by stalling segments if they are smaller than certain size. This will lower the total packets sent, but has no effect on congested network YMMV

## Slide 28: What we have covered so far
So you want to send “a buffer“ across two processes?
  Transmission + Addressing Protocols
  Basic Routing + Switching
Things we purposefully didn’t cover
  L3 switch + VLANS
  Glossed over Multicast + broadcast
Part-2:
  Traffic filtering, shaping, and tunneling