## Slide 1: Networking for non-network engineers – Part 2
Filtering and Redirecting

## Slide 2
nic-b …
nic-a
Physical Layer
Data Link
Data Link
Out: *Frame* <HEADER>BUFFER<FOOTER>
Network
Network
Out: *UDP datagram* <HEADER>BUFFER
Out: *TCP segment* <HEADER>BUFFER
Transport
Transport
Out: *Packet* <HEADER>BUFFER
APP
APP
REFRESH!

## Slide 3: Why?
Notes: Traditional Use cases
- Protecting a private network by filtering (blocking all?) ingress traffic.
Protecting a corp network by filtering egress traffic (proxy any one?)
Load balancing: by `redirecting` - balancing ingress from one receive `endpoint` to multiple servers transparently.
Protecting a server network by analyzing all ingress traffic for know attack vectors and `filtering` out bad traffic
…
New use cases
Perform rate limiting, protocols specific transformations at the ingress point (API gateway).
Mtls everywhere A->B becomes A->(`A: redirect` to MTM perform TLS)->(B: : redirect` to MTM perform TLS)->B
Kubernetes is big on redirection for built in load-balancing
…

## Slide 4
Packet Processing vs real life

## Slide 5
User Space
Kernel Space
Device
(L7) Protocol specific (payload) processing.
RAW sockets processing
DPDK *mostly* user space level packet processing
netfilters
iptables
e/BPF
via offload
How
ipvs
ebtables
Notes: I wanted the series to be OS agonistic. But for samples I choose to use linux. Almost everything I am about to cover can be done windows using different tooling, specifically “virtual filtering platform aka VFP”.
The process is the same irrespective of the traffic direction (ingress/egress).
Matching and actions are two different steps. An action can be:
Filter (drop? Or respond with an error depending on layer and protocol)
Redirect via various means
Mark (YMMV. OS specific) The mark can be used later in further actions.
Filtering/redirecting in user space such as proxies, or DPDK
Kernel space:
-- OLD STABLE:
----- netfilters: 4 triggers in kernel PREROUTING, LOCAL_IN, FORWARD, LOCAL_OUT, POST_ROUTING
----- iptables: built on top netfilters to program *actions* to be taken for every trigger. Programming is done via adding a *rule* to a list, each rule is *match*=>*action*. An action can be *terminal* such as DROP or *non terminal*
----- ebtables are like iptables but work on the link layer.
----- ipvs is a load balancer runs in the kernel. Only *redirect* actions, runs a binary tree for matching.
-- NEW
---- write code LLVM into byte code and load into the kernel. Kernel runs your code for every packet. Some h/w supports running the BPF byte code hence offloading.
For more info on DPDK https://www.dpdk.org/
This explicitly excludes traffic classification and shaping.

## Slide 6
Layer | Transmission Unit | Match On | Actions
APPLICATION | Protocol Specific Examples: HTTP r/r grpc r/r | Protocol Specific | User specific
TRANSPORT | TCP: Segment UDP: datagram | Protocol Family Port(s) IP(s) | Protocol Specific State: e.g. “new TCP connection or part of existing connection” [REDIRECT] IP/PORT SNAT or DNAT: rewrite source PORT/IP or write PORT/IP or both [FILTER] Drop: with or without a response. Or ”classify”
NETWORK | IP Packet | IP(s) * Or deep packet inspection | [REDIRECT] IP/PORT SNAT or DNAT: rewrite source PORT/IP or write PORT/IP or both [FILTER] Drop: with or without a response.
LINK | Ethernet Frame (physical network dependent) | MAC addresses | [REDIRECT]: rewrite source MAC destination MAC addresses [FILTER] DROP: …
Basic rule of the game: if (matched) then (action)
Notes: Action can be block, rewrite or other..

## Slide 7: Before we jump into iptables
An IP packet has ONE OF TWO sources:
NETWORK (i.e. from connected nic): Incoming to this host. An incoming packet are two types
  DESTINATION == MY HOST
  DESTINATION != MY HOST (when this host is acting like a router)
LOCAL: Originated from an application running on the server.
  TCP:
    Connect() generates syn packet
    Write() family of functions generates ip packets (e.g. TCP segments with PSH flag on)
    Out of band keep alive, FIN, RST, acks, and other tcp specific packets generates writes (not all packets bubbles up to app layer)
  UDP
    Write() generates ip packet that contains the UDP datagram
  IP protocol specific packets ICMP, router configuration, ARP etc all generates packets. Some are user triggered (like ping, or port scanning utilities), some are automated by the stack such as ARO

## Slide 8
https://n0where.net/how-does-it-work-iptables
On iptables
Notes: Ok that looks like a FU statement. And in a lot of ways it is, specially if you don’t decompose it, so let us break it down
Principals
1. iptables are organized as tables and chain, each table will have built in chains and user can have additional custom chain.
2. Each chain can have 0..n rules
3. chains are *fired* according to packet source, packet stage.
4. When a chain is fired, chain’s rules are checked in order if match is found, action will be executed.
5. One common rule is to *jump* from built-in chain to custom chain.
6. an *action* can be terminal or not.
To spice things up:
1. iptables have their own *modules* a module can provide *matchs* or *actions*
2. While iptables are *stateless* in nature. Each packet is matched individually. modules can make it *stateful* i.e. *is this packet part of a connection* (aka CONNTRACK module).

## Slide 9: Demo 0: filter at the IP level (iptables)
Notes: -- filter udp:
Drop packets going to 8.8.8.8

## Slide 10: Demo1: DNAT udp traffic
Notes: DNAT udp going to 1.1.1.1 to 8.8.8.8
**** RUN tcpdump on the machine while running it

## Slide 11: Demo2: SNAT udp traffic
Notes: Snatting udp traffic from vm0 to be sourced from vm1
RUN THIS ON VM1
socat - udp4-listen:5000,fork | xxd

## Slide 12: Where we are, where we are going
Understanding the TCP/IP model, layers etc
Understand transmission units for IP, TCP, UDP, Ethernet etc.
Packet filter and rewrite
What we glossed over?
  Stateful packet processing using iptables+conntrack module (exercise for the reader)
Next
  Load balancing